## Slide 1: CoAP Constrained Application Protocol
Protocolo de Capa de Aplicación para Entornos Restringidos

## Slide 2: HTTP y CoAP
Protocolo de Transferencia de Documentos Caracterizado por un estilo de arquitectura REST Representational State Transfer
Cliente: Operaciones CRUD Encabezado: POST GET PUT DELETE + Opciones de Comunicación Cuerpo: Parametros Servidor: Encabezado: Códigos de Respuesta + Opciones de Comunicación Cuerpo: Datos Opciones de Comunicación: (content-format, accept, max-age, etc)
Notes: RESTful, -ful caracterizado por... POST es el único no IDEMPOTENTE, GET es el único SEGURO

## Slide 3: CoAP vs. HTTP
HTTP: Verborrágico, todo el paquete es legible por humanos, los métodos de pedido, los códigos de respuesta y opciones de la cabecera están en ASCII. Sobre TCP: Encabezado entre 20 y 60 bytes GET /temperatura.html HTTP/1.1 \r\n Accept: application/json \r\n
CoAP: Codificado a nivel de bit. Sobre UDP: se trasladan responsabilidades a la capa de aplicación (orden de paquetes, recuperación de errores, confiabilidad, segmentación, control de congestión, pedido de retransmisión)

## Slide 4: Formato Mensaje CoAP
URI coap://dominio:5683/path?consulta#fragmento
UDP: 8 Bytes [Puerto Origen (2 Bytes), Puerto Destino (2 Bytes), Longitud: Header+Body (2 Bytes), Checksum (2 Bytes)
0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |Ver| T | TKL | 0-5 | 0-31 | Message ID | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Token (if any, TKL bytes) ... | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Options (if any) ... | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |1 1 1 1 1 1 1 1| Payload (if any) ... | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Notes: URI [coap|coaps]://dominio:5683/path?consulta#fragmento
UDP: 8 Bytes [Puerto Origen (2 Bytes), Puerto Destino (2 Bytes), Longitud: Header+Body (2 Bytes), Checksum (2 Bytes)]
Formato
Encabezado: Versión: (2 bits) Tipo: (2 bits) [0: CONfirmable, 1: NON confirmable, 2: ACKnowledgement, 3: ReSeT] Longitud Token: (4 bits) (*LTK) Código: (3 Bits) [0: Req, 1: Informativo, 2: Éxito, 3: Redirección, 4: Error Req, 5: Error Servidor) Detalle: (5 Bits) [0.01: GET, 0.02: POST, 0.03: PUT, 0.04: DELETE] [2.01: Created, 2.02: Deleted, 2.03: Valid, 2.04: Changed, 2.05: Content] [4.00: Bad Request, 4.01: Unauthorized, 4.02: Bad Option, 4.03: Forbidden, 4.04: Not Found, 4.05: Method Not Allowed, 4.06: Not Acceptable, 4.12: Precondition Failed, 4.13: Request Entity Too Large, 4.15: Unsupported Content-Format] [5.00: Internal Server Error, 5.01: Not Implemented, 5.02: Bad Gateway, 5.03: Service Unavailable, 5.04: Gateway Timeout, 5.05: Proxying Not Supported] MessageID: (2 Bytes) Token: (*LTK Bytes)
Opciones: Tipo: 4 bits (delta respecto al anterior) [1: If-Match, 3: Uri-Host 4: ETag, 5: If-None-Match, 6: Observe [0: register, 1: desregister], 7: Uri-Port, 8: Location-Path, 11: Uri-Path, 12: Content-Format: [0: text/plain; charset=utf-8, 40: application/link-format, 41: application/xml, 42: application/octet-stream, 47: application/exi, 50: application/json], 14: Max-Age, 15: Uri-Query, 17: Accept, 20: Location-Query, 35: Proxy-Uri, 39: Proxy-Scheme, 60: Size1] Longitud: 4 bits (*L) Valor: (*L Bytes)
Cuerpo: La longitud está determinado por el tamaño del datagrama.

## Slide 5: Códigos
Pedido +------+--------+ | Code | Name | +------+--------+ | 0.01 | GET | | 0.02 | POST | | 0.03 | PUT | | 0.04 | DELETE | +------+--------+
Content-Format / Accept +--------------------------+----+ | Media type | ID | +--------------------------+----+ | text/plain; | 0 | | charset=utf-8 | | | application/link-format | 40 | | application/xml | 41 | | application/octet-stream | 42 | | application/exi | 47 | | application/json | 50 | +--------------------------+----+
Opción +--------+------------------+ | Number | Name | +--------+------------------+ | 0 | (Reserved) | | 1 | If-Match | | 3 | Uri-Host | | 4 | ETag | | 5 | If-None-Match | | 7 | Uri-Port | | 8 | Location-Path | | 11 | Uri-Path | | 12 | Content-Format | | 14 | Max-Age | | 15 | Uri-Query | | 17 | Accept | | 20 | Location-Query | | 35 | Proxy-Uri | | 39 | Proxy-Scheme | | 60 | Size1 | | 128 | (Reserved) | | 132 | (Reserved) | | 136 | (Reserved) | | 140 | (Reserved) | +--------+------------------+
Respuesta +------+------------------------------+ | Code | Description | +------+------------------------------+ | 2.01 | Created | | 2.02 | Deleted | | 2.03 | Valid | | 2.04 | Changed | | 2.05 | Content | | 4.00 | Bad Request | | 4.01 | Unauthorized | | 4.02 | Bad Option | | 4.03 | Forbidden | | 4.04 | Not Found | | 4.05 | Method Not Allowed | | 4.06 | Not Acceptable | | 4.12 | Precondition Failed | | 4.13 | Request Entity Too Large | | 4.15 | Unsupported Content-Format | | 5.00 | Internal Server Error | | 5.01 | Not Implemented | | 5.02 | Bad Gateway | | 5.03 | Service Unavailable | | 5.04 | Gateway Timeout | | 5.05 | Proxying Not Supported | +------+------------------------------+

## Slide 6: Descubrimiento de Recursos
CoRE Constrained RESTfull Environments Link Format /.well-known/core
</path>; rt=“temperatura-exterior humedad”; if=“sensor” rt: tipo de recurso if: descripción de interfaz sz: tamaño máximo estimado
Grupo Multicast 224.0.1.187:5683 (experimental)
Notes: Descubrimiento de Recursos
/.well-known/core
href: enlace, rf: formato, if: interfaz, sz: tamaño de datos

## Slide 7: CoAP vs. MQTT
MQTT sigue el patrón de diseño observador, los clientes se suscriben a un broker, y el servidor publica en el broker para que transmita a los interesados de cierto topic.
CoAP permite la comunicación M2M, pero fue extendido en Septiembre de 2015 para observabilidad.
MQTT corre sobre TCP.
CoAP corre sobre UDP, pero en Agosto de 2016 se extiende con el modo de Bloque (block-wise) para resolver la segmentación.

## Slide 8: IETF RFCs
Constrained RESTful Environments (CoRE) Link Format
https://tools.ietf.org/html/rfc6690
The Constrained Application Protocol (CoAP) https://tools.ietf.org/html/rfc7252
Observing Resources in the Constrained Application Protocol (CoAP)
https://tools.ietf.org/html/rfc7641
Block-Wise Transfers in the Constrained Application Protocol (CoAP) https://tools.ietf.org/html/rfc7959
Group Communication for the Constrained Application Protocol (CoAP) https://tools.ietf.org/html/rfc7390 (experimental)

## Slide 9: Recursos
Extensión de Firefox: Copper (Cu)
coap://coap.me:5683/ coap://vs0.inf.ethz.ch:5683/

## Slide 10: Preguntas
LMGTFY
leoelzufan@gmail.com